## Slide 1: Floodplain Analysis
Kyle Michael, Aaron Steele, and Bryce Vollrath

## Slide 2
Google Maps
Notes: To make it personal, there's even an Olivet nursing student that commutes the 45-minute drive from Watseka just to attend classes here.
https://www.google.com/maps/dir/Olivet+Nazarene+University,+University+Avenue,+Bourbonnais,+IL/watseka+il/@40.9371663,-87.7803659,10z/data=!4m14!4m13!1m5!1m1!1s0x880ddd936d7ac7c7:0x2586eab6749e4043!2m2!1d-87.8723694!2d41.1549071!1m5!1m1!1s0x880d90789a3121e3:0x4c2c527a9ed61ea7!2m2!1d-87.7364218!2d40.7761465!5i2

## Slide 3
WATSEKA’S PRIMARY INTERSECTION (FEB. 2018)
Notes: Here's an aerial phot taken during the 2018 flood that covers Watseka’s PRIMARY INTERSECTION street (US Route 1 and 24)
https://www.youtube.com/watch?v=KkcZHqUfXQo (2:18)

## Slide 4: Sponsor Background
John Allhands | Mayor of Watseka, IL
Contacted us because Watseka does not have a City Engineer and Watseka is prone flooding

## Slide 5: Watseka's Need Statement
Experienced four “1% annual chance floods” in the past 11 years
45.9% of structures are within this flood area
36.1% of the population also in it

## Slide 6: Outline
Why is Watseka flooding?
Our Design Parameters
Phase 1: WWTP
Phase 2: Iroquois River
Final Recommendations
Q&A

## Slide 7
Retrieved from Watseka’s Mayor: John Allhands
Notes: Flooding in Watseka occurs because the City is located right where two large water carriers meet: the Iroquois River and Sugar Creek
On February 23, 2018, Watseka suffered from their most recent major flood.
Over 40% of the Watseka was underwater according to the blue area that symbolizes where the floodwaters were. (DeLahr, 2018)
This is the equivalent to the size of over 580 football fields completely covered in water.

## Slide 8: Why is Watseka Flooding?
-Incredibly low elevation along the Iroquois River and Sugar Creek
-Located directly downstream of a sudden increase of the Iroquois’ water elevation
-Elevation from the meeting point of the two watersheds until the Iroquois’ meets the Kankakee River is nearly flat
  Creates poor drainage
-Increase in urban development of agricultural fields
  Increasing velocity of floodwaters
  Gets to Watseka faster causing back up due to its poor drainage
-High water table (only 1-3 feet below the surface)
Google Maps
SE Kankakee
Watseka
Meeting of the Iroquois and Kankakee
Rivers

## Slide 9: Design Objectives
Our design should:
  Reduce flooding
  Be affordable
  Be durable
  Be environmentally friendly
  Use a small amount of land
  Create economic benefit
  Be able to be built quickly

## Slide 10: Design Constraints
Our design needs to:
Meet all state and federal regulations
Our design cannot:
Create additional damage
Impact towns downstream
Disrupt the Iroquois River's ecosystem
Exceed available land space
Surpass Watseka's annual budget

## Slide 11: Functional Requirements
Our design must:
Reduce flooding
Use the smallest amount of land possible

## Slide 12: Our Project’s History
Phase 1: Focusing on reducing flooding within (and in the direct vicinity) of the WWTP
Phase 2: Reducing flooding around the WWTP by focusing on reducing the flooding effects of the Iroquois (Recommendation Report Approach)

## Slide 13: Phase 1: Wastewater Treatment Plant (WWTP)
What is a wastewater treatment plant?
Why is it a concern?
Here is the current dilemma:

## Slide 14
youtube.com
DRONE PHOTO OF WATSEKA’S WWTP DURING FEBRUARY 2018 FLOOD
Notes: raised banks" instead of berms
What does the resourvoir do?
Oxidation rings
The storm gate -> entrance
https://www.youtube.com/watch?v=KkcZHqUfXQo

## Slide 15: Phase 1: Our Findings
John McBride, E.R.H. Enterprises (October 2019)
“We have operated the Watseka facility for close to 22 years, during that time there have been no non-compliance issues.”
“There has been only one instance when the discharge from the plant was limited by flooding conditions (in the past 22 years).”
Greg Marks, Watseka’s Water Sewer System Operator (October 2019)
“I believe the berm (raised bank) is still around a foot below where it should be.”

## Slide 16: Phase 1: WWTP
Repairs/updates to WWTP equipment may increase efficiency and effectiveness
Needed repairs (listed in level of urgency/cost) are outlined in Robinson Engineering's Report from March 2019
Notes: https://www.linkedin.com/company/reltd

## Slide 17: Phase 1 - Sewer System
30% of Watseka currently has a combined stormwater / sanitary sewer system
It limits the amount of stormwater the sewer system can hold
  Once the pipes are full, they overflow in the town via manholes and stormwater inlets.
Separating the remaining 30% of the sewer system will increase stormwater capacity and lessen the volume of water being sent to the WWTP

## Slide 18: Phase 1: Final Recommend-ations
Separate the Combined Sewers
Raise the Height of the WWTP’s Berms
Begin updating the WWTP’s Internal Systems

## Slide 19: Phase 2: Iroquois River
Analyze the Iroquois River
Mitigate flooding from the river to reduce flooding in Watseka
Propose multiple design options:
  Detention Pond
  Flood Bypass
  Levee

## Slide 20
LEVEE
FLOOD BYPASS
DETENTION POND

## Slide 21: Initial Thoughts
1. Detention Pond
  Would have to be large
  Mostly above ground due to 1-3 ft. water table
  Costly
2. Flood Bypass
  Needs to be long
  Mostly above ground
3. Levee
  High enough to not be overtopped
  Setback from the river
  Strong enough to withstand water forces

## Slide 22: Detention Pond: Specifications
9,000 acres (14.1 sq. mi.) and 10 ft. Deep
It should divert ~80,000 acre-ft of water.
General Detention Pond Drawing
Each line shows a 1’ elevation drop

## Slide 23
Chart: Calculating the Total Detention Volume
| 43881 | 43882 | 43883 | 43884 | 43885 | 43886 | 43887 | 43888 | 43889 | 43890 | 43891 | 43892 | 43893 | 43894 | 43895
 | 3370 | 9370 | 9340 | 8750 | 8130 | 7340 | 6430 | 5440 | 4830 | 4450 | 4390 | 4060 | 3690 | 3260 | 3020
Total Detention Volume (Area Under the Curve) = 80,000 acre-ft
Flood Stage (3100 cfs)
Peak Flow (9600 cfs)
Note: These calculations were derived from data from a measuring station along the Iroquois River approximately 20 miles away from Watseka during the February 23, 2018 flood.

## Slide 24: Flood Bypass: Specifications
17 ft. high, a 200 ft. span, and a 60° angle
Difference from peak flow to flood stage flow is ~6,000 cfs
13,000-14,000 ft. long
General Cross Section of the River Bypass Design

## Slide 25
ENLARGED VIEW
RED | Bypass
ORANGE | Bridges
Proposed Location of River Bypass

## Slide 26: Example
-The Kankakee River Study shows how channelization can increase flowrates and reduce flooding.
-Indiana straightened the Kankakee, which increased their flow rates
-The bypass (which would be used only in flooding situations) would allow for more floodwaters to flow past Watseka
KANKAKEE RIVER
STATE LINE
INDIANA
ILLINOIS

## Slide 27: Levee: Specifications
- 16,000+ ft. long
-8+ ft. high
-Determined by the Army Corp
IROQUOIS RIVER
SUGAR CREEK
PROPOSED LEVEE
Note: We are 95% confident that this is the Army Corp’s proposed levee location because it is along the floodway, 16k+ feet long, and is in their shown project location.

## Slide 28: Example
Dallas’ levee has proven very effective since 1932 (of course, it has been updated since).
51 sq. mi. of land is currently being prevented from flooding
DALLAS, TX. (CIRCA SEPT. 2017)
Notes: https://www.dallasnews.com/news/texas/2017/09/01/in-the-wake-of-harvey-dallasites-are-asking-could-catastrophic-floods-happen-here-yes/

## Slide 29: Validating: HEC-RAS
Initial Simulation (Preliminary Testing)
Used flow rate data from 2018 flood for simulation
Performed a current simulation for comparison
Then performed simulations with the levee and flood bypass using the same flow rates

## Slide 30: Validating HEC-RAS
Data inputted in HEC-Ras

## Slide 31: Validating HEC-RAS
2018 Flood Simulation

## Slide 32: Validating HEC-RAS
Flood Bypass Simulation

## Slide 33: Validating HEC-RAS
Levee Simulation

## Slide 34: Cost Estimation: Bypass
Item | Measuring Unit | Amount | Price/Unit | Total Cost
Excavating Earth | CU YD | 174465 | $12.89 | $2,248,853.85
Hauling Earth to Site | CU YD | 96224 | $18.00 | $1,732,032.00
Tree Removal | Acre | 77 | $9712.56 | $747,867.12
Cost of Land | Acre | 77 | $4112.5 | $316,662.50
Bringing Equipment to Site | Lump Sum | 1 | $200,000.00 | $200,000.00
Seeding, Erosion Control, Etc. | Lump Sum | 1 | $1,827,625.15 | $1,827,625.15
 |  |  | Total Cost | $7,073,040.62
13,000-14,000 ft. Bypass = $7.1-7.5M (plus the cost of bridges)
13,000 ft. Flood Bypass Cost Estimation

## Slide 35: Cost Estimation: Levee Detention Pond
Detention Pond (9,000 Acres, 10 ft. Deep)
$83+ M
Incredibly Large-Scale Design
Federal Share | $4.02M
Non-Federal Share | $2.14M
Total Cost | $6.16M
Army Corp’s Levee (16k+ ft., 8+ ft.)

## Slide 36: Cost Estimation: Recap
Levee: $6.16 M (only need $2.14 M)
Flood Bypass: $7.1-7.5 M (plus the cost of bridges)
Detention Pond: $83+ M

## Slide 37: Final Recommendations
Watseka should construct a levee as recommended by the Army Corps of Engineers
  Quickest time of implementation
  Short-term protection
  Least expensive option
Plans to construct a bypass should be implemented in 10-15 years
The combination of both the levee and the bypass should protect Watseka for the foreseeable future

## Slide 38: Acknowledgements
Mayor John Allhands
ONU Engineering Department
Dr. Ritzema

## Slide 39: Questions?