## Slide 1: Water Process Recyling
Adrian Barron
Kyle Serpe
Josiah Snider

## Slide 2: Agenda
Millipore Sigma
Project Background
Testing Results
Objectives and Requirements
Final Design
Validation
Acknowledgements

## Slide 3: Millipore Sigma Areas of Production
Pharmaceutical
Industrial Microbiology
Life Science
Water Purification
Labware
Sample Preparation

## Slide 4: Background
Approximately 4 million L/year of wastewater being dumped down the drain
The plant is looking to recycle the water in some capacity
Water Contains:
Proteins
Ions
The wastewater is from a wash used to clean the product inside a filter press

## Slide 5
Filter Press

## Slide 6: Need Statement
Analyzing the components within a filter press wash to recommend the best filtration method, create a flow diagram, and provide optimized tank volume calculations.

## Slide 7: Deliverables
Analyze
Analyze the components
Find
Find best filtration method
Create
Create a flow diagram
Provide
Provide optimized tank volume calculations.

## Slide 8
KNOWN COMPONENTS
Water
Proteins
Buffers (NaCl + Sodium Phosphate + NaOH)
Trace Ions (Silica, iron, calcium, magnesium, and sulfates)

## Slide 9: Testing Methods
Gas Chromatography–Mass Spectrometry (GCMS)
  Ions
Spectrophotometry
  Proteins

## Slide 10: Testing Results

## Slide 11: DESIGN OBJECTIVES
Cost effective
Environmentally conscious
Space conscious
Safe operation

## Slide 12: FUNCTIONAL REQUIREMENTS
Separates silica, proteins, salts and ions from water
Excess protein is removed from the process
Recycles water
Separation Method & Process Flow Diagram
Stores water before and after separation unit

## Slide 13: FUNCTIONAL REQUIREMENTS
Distinct from tank volume calculations
Tank Volume Calculations
Stores optimal volume
Purge Calculations
Compiles concentration and volume data for easy analysis

## Slide 14: DESIGN CONSTRAINTS
Separation Method & Process Flow Diagram
Must not bottleneck current process
Must not create large volumes of other waste
Assumptions must be displayed on the document
Tank Volume Calculations
36,000 L will enter the system over an 8-hour period in charges of 2000 L

## Slide 15: Codes and Standards
OSHA Safety Standards
Water Purity
Waste Disposal

## Slide 16: Filtration Methods Chosen

## Slide 17: Ultrafiltration and Reverse Osmosis
Ultrafiltration is used to remove purification burden from RO systems

## Slide 18: Tangential Flow Filtration
Solution flows tangentially across the membrane
Water permeates through the membrane, protein remains
Typically, requires multiple passes through the system

## Slide 19
Process Flow Diagram

## Slide 20: Tank Sizing
Calculations are done in EXCEL using a time-step model based around the TFF Permeation %
Calculated by repeated mass balances over a set of times

## Slide 21: Purge and Volume

## Slide 22: Validation and Testing
Most testing requires the design to be implemented (proper separation, optimized volumes)
Current analysis is mostly calculation / research based

## Slide 23: Benefits
Reduce water consumption
Reduce water waste
Environmentally Concious
Positive publicity

## Slide 24: Future Steps
Specification of TFF System
Implementation of System
Installation
Validation
Optimization

## Slide 25: Acknowledgements
Dr. Randall Ritzema
Scott Chase
Millipore Sigma
Dr. Bruce Heyen
Prof. Clay Bass & Dr. Joseph Schroeder

## Slide 26: Questions?