## Slide 1: Final Presentation
ONU Fish Farm Aerator Team

## Slide 2: Presentation Overview
Background
Problem Statement
Design Selection
Description of Final Design
Design Validation
Recommendations
Acknowledgements
Q & A

## Slide 3: Team Information
Jordan Hendricker
  Mechanical concentration
  Team leader
Therese Rosalez
  Civil concentration
Kylie Johnson
  Electrical Concentration
Ryan Froidcoeur
  Electrical Concentration
Faculty Mentor – Dr. Randall Ritzema

## Slide 4: Sponsor Information
AgInno Institute
Founded in 2017, their mission is to “connect the world of science and engineering with local needs in developing countries in the name of Christ”
Their primary focus is on applying the best available techniques in fields such as agriculture and clean water to improve lives in a locally sustainable manner
Primary Contact: Eric Johnson

## Slide 5: Project Description
Design a new pond aeration system for tilapia farms in Guatemala
  Increase efficiency compared to current system
    Electricity is 4x as expensive in Guatemala than the USA
  Keep fish healthy and growing without causing harm
  Intent is to equip local fish farmers to harvest their own fish and provide for their local communities
  Original plan was to travel to Guatemala to install aerator prototype with AgInno team at Misión El Faro
    Trip cancelled due to logistical issues, as well as the COVID-19 pandemic
  New plan is to give final design to AgInno for them to continue work with it

## Slide 6: Design Objectives
High Standard Aeration Efficiency (SAE)
  Defined as kilograms of dissolved oxygen in water per kilowatt-hour
  Direct relation between aeration and cost
Reliability
  A successful design will either be long-lasting and/or have parts that are easily replaceable
Healthy Ecosystem
  Cause minimal disruptions to ecosystem and promote healthy fish growth
Photos of tilapia pond and tilapia at Misión El Faro in Guatemala

## Slide 7: Functional Requirements & Design Constraints
Aerate the pond water at a rate of 5-7 mg O2/L
  This is the aeration level where tilapia are healthy and grow. They can survive at lower aeration levels, but their growth is severely stunted​
Weather/waterproof
Remain stationary on water surface
Cost
  Needs to be affordable for low-income farmers to fabricate
Locally Sourced Materials​
  All materials need to be readily available in Guatemala​
Size Requirements​
  Too large can disturb the fish​
Provide Circulation with a turbulence of no more than 1m2 ​

## Slide 8: Oxygen Transfer/Mass Balance
Accumulation = Inflow – Outflow + Generation
Key Factors
  Stocking Rate
  Water Temperature
  DO Concentration in Freshwater Influent
  Average Fish Weight
Photos of the stream that runs into the tilapia pond in Guatemala

## Slide 9: Pond Diagram
INFLUENT
EFFLUENT
CONTROL VOLUME
REAERATION
PHOTOSYNTHETIC PRODUCTION
FISH RESPIRATION
PHYTOPLANKTON RESPIRATION
NITRIFICATION
ORGANIC MATTER CONSUMPTION
Figure 2.10 - Conceptual Diagram of Pond System
DO Production
  Photosynthetic Production by Phytoplankton
  Surface Reaeration
DO Consumption
  Fish & Phytoplankton Respiration
  Organic Matter
  Nitrification
  Sediment
DO Exchanges
  Influent & Effluent Rates

## Slide 10: Design Matrix/Selection Process
Alternative | Score (SAE) [kg O2/kWh-1] | Score (Initial Cost *) | Total Score
Paddlewheel | 2 (2.5) | 1 ($320) | 25
Surface | 2 (2.5) | 1 ($320) | 25
Bubbler | 1 (1.5) | 0 ($400+) | 10
*estimated based on cost of materials

## Slide 11: Final Design Overview

## Slide 12: Paddle Design
Angled Design
  5 cm cross open face
  135°
  30 cm long
  0.3 cm thick steel
Modified version of Moore and Boyd (1991) design
Holes on surface reduce weight and drag, while increasing aeration by creating small bubbles
Spiral alignment on aluminum shaft

## Slide 13: Motor/Speed Control
Dayton 1/4 HP General Purpose AC Motor
Totally Enclosed Fan Cooled Enclosure
Installed speed controller
  Uses a potentiometer to change the current and therefore the voltage powering the motor which varies the speed

## Slide 14: Enclosure
Wood
  Easily accessible at a local store in Guatemala
  Easy to cut to the right dimensions
  Affordable
Weather/waterproof
  Coat surface with waterproofer
Current housing
Alternative design enclosure

## Slide 15: Floatation/Stabilization
Cylindrical Buoy - 5.6"X 19"
Platform- Wood-22.4"X 17" X .5"
Single Buoy can hold over 13 lbs
Total weight - over 39 lbs

## Slide 16: Testing and Validation: Experimental Design
Nitrogen purging method
Surface aeration of an 18-gallon tote
  Graph on next slide
Planned to implement aerator and measure DO level to compare to baseline reading
Planned to measure the power the motor drew during aeration process to calculate SAE value
Oxygen meter reading 0 mg O2/L indicating complete deoxygenation of the control container

## Slide 17: Testing and Validation: Experimental Design
Testing and Validation: Experimental Design

## Slide 18: Testing and Validation: Functional Requirements
Keep the dissolved oxygen level of the pond at 5-7 mg O2/L
Used methods discussed in previous slides
Mass Balance for Oxygen
Weatherproof/Waterproof
Wooden housing with hole drilled into it to protect from water and rain
  Sprayed with Thompson’s WaterSeal clear Multi-Surface Waterproofer
Waterproofing validated by inspection – water poured onto enclosure
Floatation/Stability
Planned to test tethering aerator to edges of pond
Volume of water displaced (m3) *density of water (lbs/m3)= Max weight (lbs)

## Slide 19: Testing and Validation: Design Constraints
Locally Sourced Materials
All materials used to build prototype are comparable to those available in Guatemala
Size Restriction
Used compact ¼ HP motor and kept length of device less than 3ft in length to reduce disruption to fish
Reduced Surface Agitation
Solved by installing a speed controller on motor
Reduced speed = less splashing and agitation

## Slide 20: Testing and Validation: Design Objectives
High SAE
  Installation of speed reducer to the motor to draw less power
  Moore and Boyd (1991) study recorded an SAE of 2.28 with a ½ HP motor and the angled paddle design
Low Initial Cost of Materials
  Motor is highest cost
  Initial prototype roughly $315

## Slide 21: Economic Analysis
New Paddlewheel Design
Net Present Cost = $2693.45
Annual Equivalent Cost = $476.70
Current Bubbler Design
Net Present Cost = $3478.52
Annual Equivalent Cost = $615.64
Based on
10-year analysis period
$0.29/kWh electricity in Guatemala
MARR = 12%
Speed controller reduces motor power consumption by about 50% [conservative estimate]
Photos of current bubbler

## Slide 22: Economic Analysis: Cost Breakdown
Initial Cost
  Motor = $150
  Paddles = $40
  Enclosure = $30
  Floatation = $87
  TOTAL = $317
Operational Cost
  Operate 16hr/day*
  365 days/yr
  $0.29/kWh
  TOTAL = $315.01/yr
*16 hours per day is a general estimate given time off for maintenance, harvesting, rain, etc.

## Slide 23: Recommendations
Fully test design when it is safe to do so
Intermittent operation
  Reduce operation time regardless of system implemented
Renewable energy options to power system
Developing smaller feasible motors
Test additional materials

## Slide 24: Acknowledgements
AgInno Sponsors
  Eric Johnson, Don Roe, Kirsten Roe
Dr. Randall Ritzema
  Mentor
Professor Clay Bass
Dr. Bruce Heyen
Todd Whaley
  Assisted in economic analysis

## Slide 25: References
Ali, Samir A. “DISSOLVED OXYGEN MASS BALANCE IN AQUACULTURE PONDS.” Academia.edu, www.academia.edu/8316438/DISSOLVED_OXYGEN_MASS_BALANCE_IN_AQUACULTURE_PONDS.
J. M. Moore and C. E. Boyd, “Design of small paddle wheel aerators,” Aquacultural Engineering, vol. 11, no. 1, pp. 55–69, Jan. 1992, doi: 10.1016/0144-8609(92)90021-O.

## Slide 26: Q&A
Any questions?