## Slide 1: ONU Telescope Final Design
Jake Butterfield, Nathan Eckerle,
Kamil Michorczyk

## Slide 2: Acknowledgements
Dr. Case
  Sponsoring this project
  Answering questions pertaining to requirements and objectives
Dr. Lew
  Mentoring this project
  Answering questions about vibration analysis
  Brainstorming ideas
  Providing necessary equipment

## Slide 3: Topics Covered
Project and Sponsor Background
Problem Statement
  Design Objectives and Constraints
  Functional Requirements and Specifications
Design Alternatives and Selection
  Analyses and Evaluation
  Design Matrix
Final Design Description
Testing and Validation
Conclusion/Recommendations
Q/A

## Slide 4: Sponsor Background
Our project sponsor is Dr. Stephen Case
  Associate Professor in Chemistry & Geoscience at ONU
  Director of Strickler Planetarium
  Associate Director of the University Honors program

## Slide 5: Project Background
ONU Telescope in the observatory
Vibrational issues
  This causes the telescope to produce shaky
images

## Slide 6: Need Statement and Purpose
Need:
  A method or device that will eliminate/reduce the vibrations affecting the telescope
Beneficiary:
  Dr. Case
  ONU students using the telescope for research

## Slide 7: Design Objectives
Design Objectives | Stretch Design Objectives
Diagnose vibration source(s) | Completely eliminate all vibrations
Damp vibrations enough to still image | Aesthetically pleasing
Feasible for implementation | Physically implement final design ourselves

## Slide 8: Functional Requirements & Specifications
Damp vibrations through telescope
Stabilize the image produced
Device must be easily removable for maintenance/replacement

## Slide 9: Design Constraints
Cannot alter structural integrity of the building
Telescope cannot be moved
Our design must not impede any current functions of the telescope
Stay under our budget of $900
Must keep telescope balanced
Should not impede telescope usage

## Slide 10: Vibration Diagnosis
Natural Frequency-frequency at which a system operates when disturbed
Forced Frequency-frequency of an oscillating force applied to a system
[6]

## Slide 11: Vibration Diagnosis
Concrete Slab (Which Pillar Stands On)
Front and Back of Optical Tube

## Slide 12: Design Alternatives
Three Design Alternatives as follows:
  Viscoelastic Padding
  Mechanical Damper
  Vibration Absorber

## Slide 13: Viscoelastic Padding
Viscoelastic padding under the telescope mount
Isolates telescope from the floor, and from concrete column
[1]

## Slide 14: Mechanical Damper
Uses rubber ball and spring in conjunction
[2]

## Slide 15: Vibration Absorber
Mass-spring suspension system
Three factors affect the implementation of this design:
Location of spring and mass
Spring constant (k)
Actual mass value
[3]

## Slide 16: Engineering Analyses and Evaluation
Implementing each design and testing their effectiveness falls out of the scope of this project
Therefore, the following methods were used to evaluate our designs:
  Analysis
  Research of Similar Applications
  Reasoning/Inspection

## Slide 17: Design Selection Matrix
Specifications | Weight (1-5) | Padding |  | Mechanical Damper |  | Vibration Absorber | 
 |  | Rating (1-10) | Weighted Rating | Rating (1-10) | Weighted Rating | Rating (1-10) | Weighted Rating
Reduce Vibrations | 4 | 8 | 32 | 7 | 28 | 9 | 36
Image Stability | 5 | 7 | 35 | 6 | 30 | 7 | 35
Ease of Implementation | 4 | 10 | 40 | 5 | 20 | 9 | 36
Aesthetics | 2 | 9 | 18 | 8 | 16 | 5 | 10
Cost | 3 | 10 | 30 | 5 | 15 | 10 | 30
Total (Weighted Rating) |  | 155/180 |  | 109/180 |  | 147/180 | 

## Slide 18: Final Design Selection
Originally proceeded with both the padding and vibration absorber device working in conjunction
  Pad - reduce vibrations getting to telescope
  Absorber - absorb vibrations that do get to telescope
Forced to focus solely on padding due to COVID-19
  Unable to perform necessary trial and error test for absorber

## Slide 19: Final Design Description
Sorbothane, Inc Isolation Rings
Sorbothane:
  Viscoelastic polymer
  High damping coefficient
  Designed for vibration isolation and damping
Sorbothane, Inc Engineer recommended
specific part number shown below and expressed
lifespan of up to 25 years
[4]

## Slide 20: Final Design Description
Isolation Rings adhesively attached in place
of springs
Sorbothane, Inc recommended adhesive:
  Lord 7542 Urethane Adhesive A/B
[5]

## Slide 21: Final Design Drawings cont.

## Slide 22: Final Design Drawings

## Slide 23: Final Design Cost
Following table shows price estimates:
Padding Cost | $175
Adhesive Cost | $25
Installation Labor | $200
Total Cost | $400

## Slide 24: Testing and Validation - Background Knowledge
Testing both parts of the design will involve RMS values
RMS values allows us to gauge the strength of a vibration
[7]
[8]

## Slide 25: Testing and Validation
The following is how we would test the effectiveness of the vibration isolating pad:
  Compare the amplitude of vibrations within the telescope before and after the pads are added
  Using an accelerometer, we would record vibrations for 10 seconds, for 5 separate trials
  This would then be repeated for after the pads are installed
Trial | 1 | 2 | 3 | 4 | 5 | Average RMS
With Pad (RMS) |  |  |  |  |  | 
Without Pad (RMS) |  |  |  |  |  | 

## Slide 26: Validation of Design Constraints and Objectives
Requirement | Inspection | Test | Analysis | Design Pass/Fail
Diagnose vibration source |  | X |  | Pass
Feasible and implementable |  |  | X | Pass
Under $900 budget |  |  | X | Pass
Can’t move telescope | X |  |  | Pass
Can’t restrict free motion of telescope | X |  |  | Pass
Can’t hinder use of star tracker | X |  |  | Pass

## Slide 27: Recommendations
Find appropriate mass, spring constant, and location to implement a vibration absorber
If possible, implement the design
and test to validate
Consider adding weight to
telescope
[3]

## Slide 28: Conclusions
Benefits to Client and Users:
  Telescope provides more stable images
  Useful for research
  Attract more people to studying astronomy
  Selected design stays well under budget

## Slide 29: References
[1] “19 Great Vibration Damping Pads,” The Best Industrial Supplies. [Online]. Available: http://www.thebestindustrialsupplies.com/19-great-vibration-damping-pads. [Accessed: 15-Apr-2020].
[2] A. Krishnamoorthy and M. Jayavel, “Design and Analysis of Vibration Isolation Pad of a Heavy Load Machine and to Perform the Progressive Rate Frequency Analysis,” ARPN Journal of Engineering and Applied Sciences, vol. 12, no. 16, pp. 4709–4716, Aug. 2017.
[3] D. J. Inman, Engineering vibration, 3rd. ed. Upper Saddle River, N.J: Pearson Prentice Hall, 2008.
[4] “Standard Products Guide,” Sorbothane. [Online]. Available: https://www.sorbothane.com/sorbothane-standard-products-guide.aspx. [Accessed: 15-Apr-2020].

## Slide 30: References Cont.
[5] “Lord 7542 Urethane Adhesive A/B,” Magento Commerce. [Online]. Available: https://www.chemical-concepts.com/lord-7542-a-7542-b-1-1.html. [Accessed: 15-Apr-2020].
[6] doubtnut. 2020. Explain Resonance With A Graph. Give One Example Of Resonance Fro. [online] Available at: <https://doubtnut.com/question-answer-physics/explain-resonance-with-a-graph-give-one-example-of-resonance-from-daily-life-96606410> [Accessed 15 April 2020].
[7] L. Louu, “Sound Wave Graph Compression Rarefaction - Sound Waves, HD Png Download , Transparent Png Image - PNGitem,” PNGitem.com. [Online]. Available: https://www.pngitem.com/middle/wRbbiT_sound-wave-graph -compression-rarefaction-sound-waves-hd/. [Accessed: 15-Apr-2020].
[8] “Evaluating & Using Data,” VRU, 29-Mar-2018. [Online]. Available: https://vru.vibrationresearch.com/lesson/evaluating-using-data/. [Accessed: 15-Apr-2020].

## Slide 31: What questions do you have for us?