## Slide 1: BASF Electrostatic Precipitator Waste Elimination
Alyssa Young, Brian Acosta, Austin Straw
Faculty mentor: Dr. Aram Agajanian
BASF sponsor: Mr. Seth Waits

## Slide 2: Background

## Slide 3: BASF- Sponsor
The American branch of BASF
Headquartered in Florham Park, New Jersey​
Second largest producer and marketer of chemicals and related products in North America,​
Focused on 6 key manufacturing areas ​
  “Chemicals, Materials, Industrial Solutions, Surface Technologies, Nutrition & Care and Agricultural Solutions”​
$19.7 billion in sales in 2018; second largest affiliate of BASF SE

## Slide 4: Process background- Sulfation
Acid ester waste
Electrostatic precipitator
SO3
Fatty
alcohol
Falling film reactor
Acid ester
Waste gas
Neutralization and final product production

## Slide 5: Process Background- ESP
Electrostatic precipitator (ESP) removes air impurities from the waste gas
Air impurities collect in the bottom of the ESP and form acid ester waste
Acid ester waste flows into collection tank V8; waste is then diverted into the process trench

## Slide 6: Process background- ESP Cont.

## Slide 7: Current Issues
Environmental concerns
  BASF is not currently doing anything to mitigate environment damage caused by the highly corrosive acid ester waste
Corrosion
  Acid ester is causing degradation to the current process trench which can lead to leaching and structural complications
  BASF is currently planning on redoing the process sewer for the whole of the Kankakee plant and wants to eliminate corrosion damage from the acid ester waste
  A waste elimination system needs to be developed to reduce the effect that acid ester waste has on the surrounding environment

## Slide 8: Problem description

## Slide 9: Design Objectives and Specifications
Design Objectives
Cost effective
Safe to operate
Low maintenance
Ergonomic
Be Illinois weather appropriate
Fit within the area around the ESP
Not interfere with the operation of existing systems
Exclude waste from process sewer
Be resistive to corrosion
Design Constraints

## Slide 10: Functional Requirements and Specifications
Waste processing requirements
  System can handle an average of 950 kg of acid ester waste per day
  System can handle an increase in waste production up to 1450 kg of waste per day
Environmental concerns
  Not inhibit the operation of the ESP’s
  Worker safety
System design
  Proposed design must handle all the waste during upset conditions

## Slide 11: Design Matrix
Cost
A value of one added for each predicted material
Space
Small predicted materials- add one
Large predicted materials- add two
Predicted materials
Small- pumps, piping, and level meters
Large- storage vessels
Best design will have lowest number and pass all categories
 | Cost | Space | Waste processed | Safety | Corrosive resistant | Ease of operation | Rating
Value | 0- ∞ | 0- ∞ | Pass/Fail | Pass/Fail | Pass/Fail | Pass/Fail | 0-P1P2P3P4

## Slide 12: Design alternatives

## Slide 13: Design alternatives
Recycle acid ester waste to reactor
  Reusing the acid ester waste in falling film reactor to minimize the amount of waste by creating a recycling loop
Move acid ester waste to area 90 neutralization unit
  Transport the acid ester waste to area 90 to neutralize it thus making it no longer corrosive and able to be put into the process trench
Pumping acid ester waste to one or two totes
  Pump the acid ester from V8 into one or two totes to be disposed of by a third party
Gravity fill to one or two totes
  Use gravity to make acid ester waste flow into one or two totes to be disposed of by a third party

## Slide 14: Design Matrix Cont.
Design alternative | Cost | Space | Waste processed | Safety1 | Corrosive resistant2 | Ease of operation3 | Rating
Recycle to reactor | 2 | 2 | Pass | Pass | Pass | Fail | 4- P1P2P3F4
A90 neutralization | 2 | 2 | Pass | Pass | Pass | Fail | 4- P1P2P3F4
Gravity fill to one tote | 3 | 4 | Fail | Pass | Pass | Pass | 7-F1P2P3P4
Pump to one tote | 4 | 5 | Fail | Pass | Pass | Pass | 9-F1P2P3P4
Gravity fill to two totes | 5 | 7 | Pass | Pass | Pass |  | 
Pump to two totes | 6 | 8 | Pass | Pass | Pass | Pass | 14- P1P2P3P4
12-P1P2P3F4
Pass
Fail
12-P1P2P3P4

## Slide 15: Final design

## Slide 16: Final Design- Process Flow
ESP 1
ESP 2
V8
LIT
To drain
LIT
LSH
LSH
Flow meter and transmitter
Tote 1
Tote 2
PIT

## Slide 17: Final Design- 3D drawings

## Slide 18: Final Design- Logic summary
400 kg
Valve from V8 opens and pump turns on
600 kg
~60%
Valve from V8 closed and pump turns off
V8 becomes 50% full
Valve to
tote 1 opens
Valve to
tote 2 closed
V8 becomes 10% full
Valve to
tote 1 closed
Valve to
tote 2 closed
Flow totalizer reaches 600 kg
Tote 1 is replaced, and system is reset
To drain
LSH
LSH
LSH
ESP 1
ESP 2
V8
LIT
Flow meter and transmitter
Tote 1
Tote 2
PIT
Automation starts
Automation stops

## Slide 19: Final Design-Safety measures
Set of scenarios where the system shuts down safely to allow for maintenance
  Level switch on the tote activating
  Pressure reading
    To high indicates a block after the pump
    To low indicate a block before the pump or a leak
All materials are corrosive resistant
Manual valves have locking mechanism so they cannot be moved without key verification

## Slide 20: Design validation

## Slide 21: Design Validation
Process safety review at BASF
The team completed a process safety review at BASF with various engineers and environmental health and safety officials
Comments and recommendations were added to the design to increase safety these changes include but are not limited to
  Two level sensors in V8
  Reduction of fill level in the totes to 600 kg
  Addition of steps leading to the totes to increase operator safety

## Slide 22: Materials review
Component | Type | Specifications
Piping | 316L stainless steel | 1 inch
Automated Valves | Ball valve | Fail position close
Manual Valves | Ball valve | Locking mechanism
Pump | Viking gear pump Model number GG4197 | 70 PSI output
Tote | 1000 L capacity reinforced tote | High density polyethylene

## Slide 23: Design Metrics
As seen above our final design passes in all categories and is therefore acceptable
An increase in expected cost happened due to the increase of level meters for safety purposes
All functional requirements, design objects, and design constraints are meet in our proposed design
 | Cost | Space | Waste processed | Safety | Corrosive resistant | Ease of operation | Rating
Value | 8 | 8 | Pass | Pass | Pass | Pass | 16-P1P2P3P4

## Slide 24: Cost Estimate
Installation and materials
Category | Estimated Cost
Engineering | $6,000
Instrumentation | $35,000
Valves | $3,800
Glycol piping | $8,000
Concrete and electrical | $34,000
Piping | $8000
Installation | $20,000
Total + 10% contingency | $126,000
Yearly operation
Scenario | # of totes | Total
Single tote | 1 | $400
Worst case scenario (1450kg of waste per day) | 760 | $304,000
Best case scenario (950kg of waste per day) | 500 | $200,000

## Slide 25: Conclusion
We suggest that BASF implements our solution
  Our solution cost $128,000 to implement with $200,000 in yearly operation
  Our solution does not interfere with existing operations
  Our solution does not use the process sewer thus eliminating corrosion caused by acid ester waste
The team plans on presenting the finalized design to BASF for approval

## Slide 26: Acknowledgments
We would like to thank
The BASF Kankakee site who provided us with this invaluable experience
Mr. Seth Waits who has served as our main point of contact at BASF and provided us with guidance throughout our project
Dr. Aram Agajanian and Professor Clay Bass for providing us with feedback and encouragement throughout this project

## Slide 27: Citation
“Who we are.” [Online]. Available: https://www.basf.com/us/en/who-we-are.html. [Accessed: 20-Oct-2019].

## Slide 28: Questions?