## Slide 1: Assessment of Walls with Phase Change Materials through Synergistic and Performance Measures using Experimental and Simulated Test Houses
Presented by Cory Enfield
April 7, 2022

## Slide 2: Acknowledgements
Honors Council
  Dr. Steve Case
  Dr. Dan Sharda
  Dr. Aram Agajanian
Research Mentor
  Dr. Mario Medina (University of Kansas)
Faculty Mentor
  Dr. Camilo Giraldo

## Slide 3: Overview
Background (Issue)
Background (Phase Change Materials)
Current Research
Present analysis and results
Recommendations

## Slide 4: Current Issue
US consumes about 17% of the world's energy
  Expected to increase by 50% by 2050 [1, 2]
40% of energy being consumed is attributed to buildings
  Nearly half for heating and cooling [1, 2]

## Slide 5: Proposed Solution
use of Phase Change Materials (PCMs) in buildings to help reduce energy consumption

## Slide 6: What is Phase Changing Material (PCM)?
  The materials undergoes a phase change (ex. Solid to liquid)
    Phase change occurs during latent heat absorption
  The heat is then stored until temperature drop and then the heat is released back into the space
Notes: PCMs work by absorbing thermal energy and storing it
The stored thermal energy is then released back into the environment

## Slide 7: Types of PCMs: Material and Storing
Different types of PCMS
  Organic, inorganic, eutectic
Different construction methods
  Micro-encapsulation, macro-encapsulation, and porous inclusion

## Slide 8: Latest Results on PCM in Buildings
Studies found upwards of 50% reduction of heat flux (energy entering through medium) [17-19]
Conserve upwards of 80% of energy that would have been used [23]
Most metrics focus on individual wall’s effectiveness [9]

## Slide 9: Hypothesis
Existence of a synergistic measure for PCM walls
Quantification of wall contributions
Potential for improvement of prior results

## Slide 10: Methodology: Data Acquisition
Data collected at The University of Kansas [25]
  Tested Paraffin (n-Octadecane) PCM
  PCM pouch (reflective foil)
Two test houses were tested
  Control and PCM enhanced house
Sensors attached to both sides of walls
Test Duration: 2 Days
Notes: Typical North American residential construction methods: The houses were both outfitted with a south-facing window, chilled water cooler, asphalt shingles, and insulated with a fiberglass and cellulose mixture. Sensors: Type T thermocouples, relative humidity transducers, and Thermal Flux Meters

## Slide 11
Houses were simulated based on the data from the KU experiment
  16 simulated houses were created by use of binary numbers (0-15)
    1 = 0001
    2 = 0010
    Control wall = 0
    PCM wall = 1
All data manipulation was done in MATLAB 2021a (MathWorks, MA)
Data Analysis
Methodology

## Slide 12: Measures Collected
Metrics used per day per house/simulation
Heat flux for simulated houses added together
  Maximum heat flux
  Total heat
  Time delays (beginning of positive heat flux, peaks, and end)
  Average heat flux
  Standard Deviation
Notes: Max: The peak amount of heat entering the house
Total: The integral of the positive heat entering the house
Time Delays: measured from the point of heat entering (first positive value) to the point where no more heat enters. Delays could be at the start, peak, or end of the positive values
Average: average values for heat flux
Standard deviation: how dispersed or different the data is

## Slide 13: Wall Contributions
One wall is held constant to determine contribution
  In the example it’s the North wall

## Slide 14: Results

## Slide 16
Max Heat Flux
Time Delay Max
Time Delay Start
Time Delay End
Heat
Heat Flux Average
Heat Flux Standard Deviation
Notes: Max Heat: As more PCM is added, the graph trends down
Sim. 13 (1101) had results comparable to the Full PCM house
As seen later, different wall combinations present better results for different measures
Max Delay: Time delays seen only in the first day
Simulated houses with 2 or more PCM walls were most likely to see a delay
Start Delay: Day 1: Sims. 6, 7, & 14 had comparable time delays to the full house, and each had the east wall
Day 2: Sims 2-7 and 10-15 comparable time delays
Each of the day 2 sims. Had either the east wall or a combination of west and south walls
End Delay: Day 1: sim 7, 13, and 14 had similar end delaysMore PCM equated to larger end delays
Simulations with 3 PCMs showed the highest time delays outside of the Full house
Heat: 3 PCM sims had most comparable results
WS or WE had the best 2 PCM combination for reducing heat
Average Heat: Lower average = less heat passing through the house
East wall bring the average down and the WS combination had a similar effect
Sim 7 had comparable results to full
Stdv: 2 or more PCM walls had lower deviations
Less deviation = more consistent indoor temperature
Sim 11 and 13 had comparable Standard Deviations to the full house. Had W and S walls

## Slide 18
Simulations without the East PCM wall began heating sooner
Simulated houses with 3 PCM walls had lower peaks
Addition of the south kept peaks down
West wall addition reduced the back half of the curve
Notes: 1st point: Each of these simulations did not have the east wall
5th point: It would stay in cooler and warmer temperatures longer
  This means it helped keep temperature more consistent

## Slide 20: Notables
For Peak reduction and standard Deviation, the west wall contributed
For the average heat flux, the east wall had the highest difference followed by the south wall
North wall contributed the least in almost all measures

## Slide 22: Notables
South & East walls provided the largest start time delay
South wall contributed the most when it came to time delays
There was no one wall that helped reduce peak times
Notes: South delayed both the start and the end the most

## Slide 23: Final Conclusions
South wall was the most consistent with benefits
For start time delays the East wall would be the most beneficial
The West wall is best for the later half of the day
The best simulations included Combinations of the East, West, and South walls
  North contributed little to the main goal
More PCM = More reduction = More expensive to retrofit

## Slide 25: References
[1] “Consumption & Efficiency - U.S. Energy Information Administration (EIA).” https://www.eia.gov/consumption/index.php (accessed Oct. 17, 2021).
[2] “Department of Energy.” https://www.energy.gov/ (accessed Oct. 17, 2021).
[3] Y. Huang and J. Niu, “A review of the advance of HVAC technologies as witnessed in ENB publications in the period from 1987 to 2014,” Energy Build., vol. 130, pp. 33–45, Oct. 2016, doe: 10.1016/j.enbuild.2016.08.036.
[4] H. Mehling and L. F. Cabeza, Heat and cold storage with PCM: An up to date introduction into basics and applications. Berlin, Heidelberg: Springer Berlin Heidelberg, 2008. doi: 10.1007/978-3-540-68557-9.
[5] V. V. Tyagi and D. Buddhi, “PCM thermal storage in buildings: A state of art,” Renew. Sustain. Energy Rev., vol. 11, no. 6, pp. 1146–1166, Aug. 2007, doi: 10.1016/j.rser.2005.10.002.
[6] “Phase change materials for thermal energy storage,” Prog. Mater. Sci., vol. 65, pp. 67–123, Aug. 2014, doi: 10.1016/j.pmatsci.2014.03.005.
[7] American Concrete Institute, How to Integrate Phase Change Materials in Construction Materials, (Jun. 11, 2020). Accessed: Apr. 06, 2021. [Online Video]. Available: https://www.youtube.com/watch?v=i_4ip4MetLk
[8] OER Services, “Applications of Phase Change Materials for Sustainable Energy,” in Sustainable Energy Systems, Online: Lumen Candela. [Online]. Available: https://courses.lumenlearning.com/suny-sustainability-a-comprehensive-foundation/chapter/applications-of-phase-change-materials-for-sustainable-energy/
[9] A. Evers, “Development of a Quantitative Measure of the Functionality of Frame Walls Enhanced with Phase Change Materials Using a Dynamic Wall Simulator,” PhD, Univesity of Kansas, 2007. [Online]. Available: https://kuscholarworks.ku.edu/bitstream/handle/1808/4164/umi-ku-2679_1.pdf?sequence=1&isAllowed=y
[10] L. Shilei, Z. Neng, and F. Guohui, “Impact of phase change wall room on indoor thermal environment in winter,” Energy Build., vol. 38, no. 1, pp. 18–24, Jan. 2006, doi: 10.1016/j.enbuild.2005.02.007.
[11] F. Kuznik and J. Virgone, “Experimental assessment of a phase change material for wall building use,” Appl. Energy, vol. 86, no. 10, pp. 2038–2046, Oct. 2009, doi: 10.1016/j.apenergy.2009.01.004.
[12] X. Sun, M. A. Medina, and Y. Zhang, “Potential Thermal Enhancement of Lightweight Building Walls Derived From Using Phase Change Materials (PCMs),” Front. Energy Res., vol. 7, 2019, doi: 10.3389/fenrg.2019.00013.
[13] X. Sun, M. A. Medina, K. O. Lee, and X. Jin, “Laboratory assessment of residential building walls containing pipe-encapsulated phase change materials for thermal management,” Energy, vol. 163, pp. 383–391, Nov. 2018, doi: 10.1016/j.energy.2018.08.159.
[14] R. Vicente and T. Silva, “Brick masonry walls with PCM macrocapsules: An experimental approach,” Appl. Therm. Eng., vol. 67, no. 1, pp. 24–34, Jun. 2014, doi: 10.1016/j.applthermaleng.2014.02.069.
[15] Y. Zhang, X. Sun, and M. A. Medina, “Experimental evaluation of structural insulated panels outfitted with phase change materials,” Appl. Therm. Eng., vol. 178, p. 115454, Sep. 2020, doi: 10.1016/j.applthermaleng.2020.115454.
[16] B. Nghana and F. Tariku, “Phase change material’s (PCM) impacts on the energy performance and thermal comfort of buildings in a mild climate,” Build. Environ., vol. 99, pp. 221–238, Apr. 2016, doi: 10.1016/j.buildenv.2016.01.023.
[17] X. Shi, S. A. Memon, W. Tang, H. Cui, and F. Xing, “Experimental assessment of position of macro encapsulated phase change material in concrete walls on indoor temperatures and humidity levels,” Energy Build., vol. 71, pp. 80–87, Mar. 2014, doi: 10.1016/j.enbuild.2013.12.001.
[18] K. O. Lee, M. A. Medina, E. Raith, and X. Sun, “Assessing the integration of a thin phase change material (PCM) layer in a residential building wall for heat transfer reduction and management,” Appl. Energy, vol. 137, pp. 699–706, Jan. 2015, doi: 10.1016/j.apenergy.2014.09.003.
[19] E. Meng, H. Yu, and B. Zhou, “Study of the thermal behavior of the composite phase change material (PCM) room in summer and winter,” Appl. Therm. Eng., vol. 126, pp. 212–225, Nov. 2017, doi: 10.1016/j.applthermaleng.2017.07.110.
[20] J. Kosny, N. Shukla, and A. Fallahi, “Cost Analysis of Simple Phase Change Material-Enhanced Building Envelopes in Southern U.S. Climates,” National Renewable Energy Lab. (NREL), Golden, CO (United States), NREL/SR-5500-55553; DOE/GO-102013-3692, Jan. 2013. doi: 10.2172/1067934.
[21] X. Sun, Q. Zhang, M. A. Medina, and K. O. Lee, “Energy and economic analysis of a building enclosure outfitted with a phase change material board (PCMB),” Energy Convers. Manag., vol. 83, pp. 73–78, Jul. 2014, doi: 10.1016/j.enconman.2014.03.035.
[22] H. J. Akeiber, S. E. Hosseini, H. M. Hussen, M. A. Wahid, and A. Th. Mohammad, “Thermal performance and economic evaluation of a newly developed phase change material for effective building encapsulation,” Energy Convers. Manag., vol. 150, pp. 48–61, Oct. 2017, doi: 10.1016/j.enconman.2017.07.043.
[23] W. A. Qureshi, N.-K. C. Nair, and M. M. Farid, “Impact of energy storage in buildings on electricity demand side management,” Energy Convers. Manag., vol. 52, no. 5, pp. 2110–2120, May 2011, doi: 10.1016/j.enconman.2010.12.008.
[24] A. Bland, M. Khzouz, T. Statheros, and E. I. Gkanas, “PCMs for Residential Building Applications: A Short Review Focused on Disadvantages and Proposals for Future Development,” Buildings, vol. 7, no. 3, Art. no. 3, Sep. 2017, doi: 10.3390/buildings7030078.
[25] M. A. Medina, K. O. Lee, X. Jin, and X. Sun, “On the Use of Phase Change Materials (PCMs) in Building Walls for Heat Transfer Control and Enhanced Thermal Performance,” presented at the Asain-Pacific Economic Cooperation Conference, May 2013.